Ford MUSTANG – EUROPEAN Specifications

BODY

| Construction | Unitised welded steel body, aluminium bonnet and front wings |
| --- | --- |
| Body Styles | Fastback and Convertible; Left-hand and Right-hand Drive |
| Final assembly location | Flat Rock, Michigan, USA |

ENGINE

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Configuration | Aluminium block and head | Aluminium block and heads |
| Intake manifold | Composite shell-welded with runner pack | Composite shell-welded with runner pack and charge motion control valves |
| Exhaust manifold | Three-port integrated into aluminium head | Stainless steel tubular manifold |
| Valvetrain | DOHC, four valves per cylinder, twin independent variable camshaft timing | DOHC, four valves per cylinder, twin independent variable camshaft timing |
| Valve diameter/lift | Intake 31 mm/8.31 mm Exhaust 30 mm/7.42 mm | Intake 37.3 mm/13 mm Exhaust 31.8 mm/13 mm |
| Pistons | Cast aluminium | Cast aluminium |
| Connecting rods | Forged steel | Forged steel |
| Ignition | Distributor-less with coil-on-plug | Distributor-less with coil-on-plug |
| Bore x stroke | 87.55 mm x 94 mm | 92.2 mm x 92.7 mm |
| Displacement | 2300 cc | 4951 cc |
| Compression ratio | 9.5:1 | 11.0:1 |
| Engine control system | PCM | PCM |
| Power | >309 PS (227 kW) @ 5500 rpm (projected, US Spec) | >426 PS (313 kW) @ 6500 rpm (projected, US Spec) |
| Torque | >407 Nm @ 2500-4500 rpm (projected, US Spec) | >529 Nm @ 4250 rpm (projected, US Spec) |
| Fuel capacity | 59 L | 61 L |
| Fuel delivery | Direct injection | Sequential multiport electronic |
| Oil capacity | 5.7 L 5W-30 with filter (16,000-km service interval) | 7.6 L 5W-20 with filter (16,000-km service interval) |

DRIVETRAIN

| Layout | Rear-wheel drive with limited-slip differential |
| --- | --- |

TRANSMISSION

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Standard | Six-speed manual with Hill Start Assist |
| Gear ratios |
| First | 4.236 | 3.657 |
| Second | 2.538 | 2.430 |
| Third | 1.665 | 1.686 |
| Fourth | 1.238 | 1.315 |
| Fifth | 1.00 | 1.00 |
| Sixth | 0.704 | 0.651 |
| Final drive | 3.55:1 | 3.55:1 |
| Optional | Six-speed automatic with paddle shifters |
| Gear ratios |
| First | 4.17 |
| Second | 2.34 |
| Third | 1.52 |
| Fourth | 1.14 |
| Fifth | 0.87 |
| Sixth | 0.69 |
| Final drive | 3.55:1 |

SUSPENSION

| Front | Double-ball-joint independent MacPherson strut and tubular stabiliser bar |
| --- | --- |
| Rear | Integral-link independent with coil springs, solid stabiliser bar, and twin-tube dampers (2.3-litre EcoBoost) or mono-tube dampers (V8) |

STEERING

| Type | Electric power-assisted steering with rack-and-pinion gear |
| --- | --- |
| Ratio | 16:1 |
| Turning circle, curb-to-curb | 12.2 m |

BRAKES

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Type | Four-wheel power disc brakes with four-sensor, four-channel anti-lock braking system and AdvanceTrac electronic stability control | Four-wheel power disc brakes with four-sensor, four-channel anti-lock braking system and AdvanceTrac electronic stability control |
| Front | 352 mm x 32 mm vented discs, four-piston 46 -mm fixed aluminium callipers | 380 mm x 34 mm vented discs, Brembo six-piston 36 mm fixed aluminium callipers |
| Rear | 330 mm x 25 mm vented discs, single-piston 45 mm floating iron callipers, integral parking brake | 330 mm x 25 mm vented discs, single-piston 45 mm floating iron callipers, integral parking brake |

WHEELS AND TYRES

| Standard | 255/40 R19 Tyres, 19 inch x 9 inch aluminium wheels | Front: 255/40 R19 Tyres, 19 inch x 9 inch aluminium wheels Rear: 275/40 R19 Tyres, 19 inch x 9.5 inch aluminium wheels |
| --- | --- | --- |

DIMENSIONS

|  | Fastback | Convertible |
| --- | --- | --- |
| EXTERIOR |
| Wheelbase | 2720 | 2720 |
| Overall length | 4784 | 4784 |
| Overall width | 1916 | 1916 |
| Overall height | 1381 | 1394 |
| Track, front/rear | 1570/1637 | 1570/1637 |
| INTERIOR |
| Seating capacity | Four | Four |
| Front headroom | 955 | 956 |
| Front legroom – maximum | 1131 | 1131 |
| Front shoulder room | 1430 | 1430 |
| Front hip room | 1395 | 1395 |
| Rear headroom | 884 | 907 |
| Rear legroom | 777 | 783 |
| Rear shoulder room | 1327 | 1135 |
| Rear hip room | 1203 | 1111 |

CAPACITIES

| Passenger volume | 2392 L | 2287 L |
| --- | --- | --- |
| Cargo volume | 383 L (based on US SAE Spec) | 324 L (based on US SAE Spec) |

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

# # #

About Ford Motor Company

Ford Motor Company, a global automotive industry leader based in Dearborn, Mich., manufactures or distributes automobiles across six continents. With about 180,000 employees and 65 plants worldwide, the company’s automotive brands include Ford and Lincoln. The company provides financial services through Ford Motor Credit Company. For more information about Ford and its products worldwide please visit www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 47,000 employees at its wholly owned facilities and approximately 67,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 22 manufacturing facilities (13 wholly owned or consolidated joint venture facilities and nine unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.

Contacts: Sandra van Tongern Ford of Europe +49 (0) 221 901 8794 svantong@ford.com