Contact extension for light grid applications

The PSR-URM4L contact extension device from Phoenix Contact is highly suited for light grid applications. It allows users to efficiently process safety-related OSSD signals of a light grid as floating contacts, therefore supporting safety-relevant circuits up to PLe.

The contact extension device is specifically designed for use with Electro-sensitive protective equipment (ESPE) such as light grids. Such systems normally include switched-mode OSSD signals that make it possible to detect cross-circuits in the cabling. The relay is resistant to test pulses generated by the CFSE. This allows for the implementation of applications that comply with PLe or SIL 3 without the need to reconnect the device to the external device monitoring circuit.

Ends

Sept 2013

PR4554GB

Phoenix Contact Ltd

Halesfield 13

Telford

Shropshire

TF7 4PG

Tel: 0845 881 2222

Fax: 0845 881 2211

www.phoenixcontact.co.uk

info@phoenixcontact.co.uk

For further information on this press release please contact:

Phoenix Contact Ltd, Halesfield 13, Telford, TF7 4PG.

Becky Smith DD 01952 681756 bsmith@phoenixcontact.com