PRESS RELEASE    Ref: 3.1057F                                              21st March 2018

Photo Ref: 3.1057F

Some of the completed valve, actuator and Pressure Safe packages produced by Rotork Singapore for the first onshore wellhead production order.

Rotork assists Singapore-based oil and gas consultancy in major African project

The introduction of an in-house hydrostatic test facility at Rotork Singapore is making an important contribution to winning new contracts. One of the first orders is from Singapore-based marine, oil and gas consultancy Praj Marine (PMC) for a project in Africa.

Rotork’s ability to provide third-party witnessed hydrostatic testing, combined with the supply of specialised failsafe actuation solutions on short lead times, have enabled PMC to secure new contracts for onshore wellhead and gas projects.

Specialised actuation is required because there is no power source available for valve control on the wellhead production flow line, water injection and disposal installations. Rotork’s successful and innovative solution comprises GH and RH hydraulic spring-return actuators operated by Pressure Safe self-contained manually operated hydraulic power packs.

A hydraulic hand pump on the compact Pressure Safe power pack is used to energise the actuator and compress the failsafe spring, holding the valve in the desired open or closed position until a failsafe signal is received, at which point the spring will immediately drive the valve to the safe position.

Failsafe operation of Pressure Safe units can be triggered by electrical signals, high or low pressure pilots or fire sensors, enabling the reliable fulfilment of many ESD (Emergency Shutdown) and pressure related protection duties in the oil, gas, petrochemical and pipeline industries.

The order included mounting the actuators on 75 mm (3") and 150 mm (6") Class 1500 flanged ball valves.

END

Continued…

Ref: 3.1057F                                               21st March 2018

Rotork assists Singapore-based oil and gas consultancy in major African project

Issued on behalf of:	Rotork PLc

Brassmill Lane, Bath, BA1 3JQ, UK				Tel:  +44 (0)1225 733200

information@rotork.com

www.rotork.com

Contacts:	Rotork – Sarah Kellett (sarah.kellett@rotork.com)

FTPublicity – Mark Clark (ftpublicity@aol.com)

Background Notes for Editors:

For over 60 years, engineers have relied upon Rotork for innovative and dependable flow control solutions. Rotork products and services are helping companies in the oil & gas, water & wastewater, power generation, marine, mining, food, pharmaceutical and chemical industries around the world to improve efficiency, assure safety and protect the environment.

Issued by: FTPublicity

Corsham, SN13 9XH, UK

Tel: +44 (0)1249 714447

www.ftpublicity.co.uk